## Slide 1: TAT-C O&C walkthrough
March 27, 2019
NASA Goddard Space Flight Center

## Slide 2: Outline
Highest-level functional view
Structural view
End-to-end functional view
  Initialization
  Propagation
  Coverage checking
    Control
    Checking visibility of a point
  Post Processing
  Questions??

## Slide 3: High-Level View
Pseudocode (driver)
Propagate orbit to initial time
While (not end of time range)
Accumulate coverage data
Advance clock by propagation step size
Propagate state to new time
End loop
Post-process
Notes:
There are interpolation & non-interpolation variants of Accumulate code.
When interpolating, there is an inner loop driven by interpolator step size, which in turn depends on event detection granularity
Pseudocode
AccumulateCoverageData()
Get spacecraft state
// interpolation option is found here
Store time data
CheckPointCoverage(time, EFposition)
CheckPointCoverage()
Perform dot product (feasibility) checks
For each point in points of interest loop
Compute satellite-to-target vector in inertial frame
if (s/c has sensor) // only 1 allowed at this point
call s/c to check target visibility for the sensor
else
do horizon test to see if s/c is over horizon
if (point is in view)
store data for post processing
End loop

## Slide 4: O&C dependency structure
Light colored objects are used by larger Orbit system
Orbit system also calls constructors for the dark colored objects
  Or is given these objects by the test driver SystemTestAnalysis.cpp
  See next slide on initialization
Spacecraft
Coverage
Checker
Sensor
Attitude
Conical
Custom
Rectangular
Orbit State
Propagator
1,..n
1,..n
Interpolator
Absolute Date
Nadir Pointing Attitude
1,..n
1,..n
LaGrange
Interpolator
PointGroup
Visible POI
Report
Interval Event Report
Earth

## Slide 5: Initialization Sequence
Objects needed are in parentheses
  LagrangeInterpolator()
  Earth()
  AbsoluteDate()
  OrbitState
  Sensor() //abstract class, see next slide for subclasses
  NadirPointingAttitude() // subclass of Attitude
  Spacecraft(Attitude,AbsoluteDate,OrbitState, LaGrangeInterpolator)
    // sensors added via AddSensor
  Propagator(Spacecraft)
  PointGroup() // provides functions to add points
  CoverageChecker(PointGroup,SpaceCraft)

## Slide 6: Sensor subclasses
Conical sensor
  One angle, specifying cone angle from boresight
Rectangular sensor
  Two angles, specify width and height angles from boresight
Custom sensor
  Sequence of cone and clock angles defining perimeter of FOV
  Complex algorithm to check visibility

## Slide 7: Propagation
Classes
  Propagator, Spacecraft, Sensor (and subclasses), NadirPointingAttitude, Earth, LaGrangeInterpolator, OrbitState, AbsoluteDate
More complex data structures
  In interpolators, arrays of points to interpolate
  In CustomSensor, arrays of cone & clock angles
More complex functions
  Propagate() and PropagateOrbitalElements() – models two body problem, including oblateness of Earth (J2) and optionally atmospheric drag
  ComputePeriapsisAltitude() – computes values needed for drag modeling
  Sensor->CheckTargetVisibility() –
    Simple bounds check for conical and rectangular sensors
    Complex line intersection algorithm for CustomSensor
    Used by CoverageChecker invoking Spacecarft->CheckTargetVisibility()

## Slide 8: Coverage checking: Classes
Classes
  CoverageChecker
    Manages accumulation of interval data
    Provides post processing functions
  PointGroup
    Set of points on surface of central body, in body-fixed coordinates
    Represented as latitude/longitude or as unit vector
  VisiblePOIReport
    Contains azimuth and zenith for spacecraft and sun
    Contains range for spacecraft
  IntervalEventReport
    Contains start and end time for interval a given point is visible
    Optionally contains a vector of VisiblePOIReport
    Used by ProcessCoverageData() to generate reports

## Slide 9: CoverageChecker: Data Structures
pointGroup – pointer to the PointGroup passed into CoverageChecker constructor
pointArray – body fixed position of each point in pointGroup
dateData – an array containing date & time of each event location step
timeSeriesData – contains a vector of indices into dateData for each point in pointGroup
discreteEventData – contains a vector of visiblePOIReport for each point in pointGroup
numEventsPerPoint – array containing the number of times each point is in the sensor FOV

## Slide 10: CoverageChecker functions: CheckPointCoverage()
This is same function as shown in high level view, pseudocode now refers to actual data structures
FOV = field of view
This function uses inertial and ECEF coordinate frames, does not worry about attitude or sensor frame (Spacecraft class does that)
For each POI in pointGroup loop
if (POI passes dot product check) then
check target visibility
if (spacecraft is in view) then
store time index in timeSeriesData /
for the POI
store POI in list of points in FOV
if (target geometry option is on) then
create a VisiblePOIReport
store report in discreteEventData /
for the POI
end if // target geometry option
end if // spacecraft in view
end if // dot product check
End loop
Return list of points in sensor FOV

## Slide 11: CoverageChecker functions: ProcessCoverageData()
Use of data structures
  Intervals are identified by series of consecutive time indices
  First and last index is used to look up start and end time in dateData array
VisiblePOIreport
  Remember, generating this data is optional, so intervalEventRecord may reduce to list of start and end times
test/SystemTestAnalysis.cpp
  Contains example of how post processed data may be used.
For each POI in pointGroup loop
if (numEventsPerPoint[POI] > 2) then
set start time
look for intervals s/c is in view
if (end of interval) then
isEnd = true
set end
end if
if (isEnd) then
// create intervalEventReport
set start & end times
add VisiblePOIrecords // if created
add intervalEventReport to reports
isEnd = false
end if
End loop
Return reports

## Slide 12: Summary
Capabilities
  Propagator contains models for position and velocity over time
  Spacecraft contains or uses key classes such as Sensor or LaGrangeInterpolator
  Coverage checker determines when each point is in sensor FOV
Limitations/Potential follow-on task work
  One sensor per spacecraft; hooks exist for multiple sensors that shouldn’t be hard to add to modeling.
  Design is for one spacecraft; workaround is to have one CoverageChecker/Spacecraft/Propagator set per spacecraft. Probably should refactor next year.

## Slide 13: Questions?
Q1. Is Nadir-Pointing attitude restricted to a specific definition of axes? The code reverses y and x axes from the usual +z to center of earth, +y is negative orbit normal, +x completes triad.
Your questions?